## Slide 1
Hardware Virtual Texturing
Graham Sellers, AMD
graham.sellers@amd.com
@grahamsellers

## Slide 2: Hardware Virtual Texturing
Virtual Texturing
  Virtual textures are textures that are not all in video memory at one time
  Software Virtual Textures (SVTs) have been around for a while
  The goal is to provide support in hardware

## Slide 3: Virtual Textures
Divide texture up into tiles
  Commit only used tiles to memory
  Store data in separate physical texture
Virtual Texture
Physical Texture

## Slide 4: Virtual Textures
Memory requirements set by number of resident tiles, not texture dimensions
RGBA8, 1024x1024, 64 tiles
 | Virtual | Physical
Memory | 4096 kB | 1536 kB

## Slide 5: Virtual Textures
Use indirection table to map virtual to physical
  This is also known as a page table

## Slide 6: Virtual Textures
Software Virtual Textures
uniform sampler2D samplerPageTable; // page table texture
uniform sampler2D samplerPhysTexture; // physical texture
in vec4 virtUV; // virtual texture coordinates
out vec4 color; // output color
vec2 getPhysUV(vec4 pte); // translation function
void main()
{
vec4 pte = texture(samplerPageTable, virtUV.xy); // (1)
vec2 physUV = getPhysUV(pte); // (2)
color = texture(samplerPhysTexture, physUV.xy); // (3)
}

## Slide 7: GPU Virtual Memory
Virtual Memory for GPUs
  Very similar to virtual memory on CPUs
  Page tables in video memory
  Address translation handled by hardware

## Slide 8: GPU Virtual Memory
texture(sampler, uv);
Texture Unit
uv
virtual address
Memory Controller
Page Table
…
Physical Memory
virtual address
physical address
physical address
data
data
data

## Slide 9: Sparse Textures
Paging
  The process of making resources resident in GPU-visible memory
  Handled by the operating system or lower level system components
  Non-sparse resources paged in and our with resource granularity

## Slide 10: Sparse Textures
Sparse textures depend on 3 core components:
  GPU virtual memory
  Shader core feedback
  Software driver stack

## Slide 11: Sparse Textures and GPU Virtual Memory
Texture Unit
  UV to virtual address translation
  Hardware filtering
  Cache
Memory Controller
  Virtual to physical address translation
  Page table management
  Cache

## Slide 12: Virtual Textures
Software Virtual Textures (Recap)
uniform sampler2D samplerPageTable; // page table texture
uniform sampler2D samplerPhysTexture; // physical texture
in vec4 virtUV; // virtual texture coordinates
out vec4 color; // output color
vec2 getPhysUV(vec4 pte); // translation function
void main()
{
vec4 pte = texture(samplerPageTable, virtUV.xy); // (1)
vec2 physUV = getPhysUV(pte); // (2)
color = texture(samplerPhysTexture, physUV.xy); // (3)
}

## Slide 13: Sparse Textures and GPU Virtual Memory
Hardware Virtual Textures
uniform sampler2D samplerPRT // partially-resident texture
in vec4 virtUV; // virtual texture coordinates
out vec4 color; // output color
void main()
{
color = vec4(0.0);
sparseTexture(samplerPRT, virtUV.xy, color); // (3)
}

## Slide 14: Sparse Textures and Shaders
Virtual Address Space
  Segmented into 64KiB pages
  Each tile can be mapped (resident) or unmapped (non-resident)
  Mapping controlled by the driver and application
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 15: Sparse Textures and Shaders
texture(sampler, uv);
Texture Unit
uv
virtual address
Memory Controller
Page Table
…
Physical Memory
virtual address
NACK
NACK
NACK

## Slide 16: Sparse Allocations
What can be sparse?
  Any tile-aligned region of a texture level

## Slide 17: Sparse Allocations
What can be sparse?
  Full mip-levels

## Slide 18: Sparse Allocations
What can be sparse?
  Cube map faces

## Slide 19: Sparse Allocations
What can be sparse?
  Any combination of the above, plus...
    Slices of 3D textures, array layers, etc., etc.
  ... so long as it meets tile alignment requirements

## Slide 20: Sparse Textures and Shaders
NACKs in shaders
void main()
{
vec4 outColor = vec4(1.0, 1.0, 1.0, 1.0);
int code = sparseTexture(sampler, texCoordVert.xy, outColor);
if (sparseTexelResident(code))
{
// data resident
gl_FragColor = vec4(outColor.rgb, 1.0);
}
else
{
// NACK
gl_FragColor = vec4(1.0, 0.0, 0.0, 1.0);
}
}

## Slide 21: Sparse Textures – Drivers
Driver responsibilities
  Create and destroy sparse resources
  Map and un-map tiles
  Back virtual allocations with physical allocations

## Slide 22: Sparse Textures – Drivers
Backing storage
  A set of physical allocations containing texture data
    Don’t want one physical allocation per tile
    Driver manages pools of tiles
  Each application will have different requirements

## Slide 23: Physical Texture Pools
0
1
2
3
x
16
17
18
19
x
12
13
14
15
x
x
x
x
x
x
8
9
10
11
x
20
21
22
23
x
28
29
30
31
x
x
x
x
x
x
4
5
6
7
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
24
25
x
x
x
26
27
x
x
x
x
x
x
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Sparse Texture
Chunk 1
Chunk 2

## Slide 24: Physical Texture Pools
0
1
2
3
x
16
17
18
19
x
12
13
14
15
x
x
x
x
x
x
8
9
10
11
x
20
21
22
23
x
28
29
30
31
x
x
x
x
x
x
4
5
6
7
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
24
25
x
x
x
26
27
x
x
x
x
x
x
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
Sparse Texture
Chunk 1
Chunk 2
x
x
x
x

## Slide 25: Tile Pool Management
Let the application deal with it!
  Introduce new objects called tile pools
  Non-virtual allocations
    Huge arrays of tiles
    Look like array textures
  Application gets to ‘place’ tiles into textures

## Slide 26: Tile Pool Management
Tile pools enable several things
  Tight, application controlled memory management
  Aliases – using the same tile at multiple places
  Sharing a single pool amongst many virtual textures
  Wang tiles in hardware

## Slide 27: Hardware Virtual Textures
Summary
 | SVTs | HVTs
Address translation | Shader code | HW page table
Filtering | HW + shader code | HW only
# of texture fetches | 2, dependent | 1
Supported formats | The ones implemented | All supported by HW
Supported texture types | The ones implemented | All supported by HW

## Slide 28: Accessing the Feature
Exposed through OpenGL extensions
  GL_AMD_sparse_texture
    Enables basic driver managed virtual textures
  GL_AMD_texture_tile_pool
    Adds tile pool support
    Still in the pipeline...

## Slide 29: Sparse Textures in OpenGL
Use of immutable texture storage
Existing OpenGL immutable storage API
  Declare storage, specify image data
GLuint tex;
glGenTextures(1, &tex);
glBindTexture(GL_TEXTURE_2D, tex);
glTexStorage2D(GL_TEXTURE_2D, 10, GL_RGBA8, 1024, 1024);
glTexSubImage2D(GL_TEXTURE_2D, 0, 0, 0, 1024, 1024,
GL_RGBA, GL_UNSIGNED_BYTE, data);

## Slide 30: Sparse Textures in OpenGL
Use of sparse texture storage
glTexStorageSparseAMD is a new function
GLuint tex;
glGenTextures(1, &tex);
glBindTexture(GL_TEXTURE_2D, tex);
glTexStorageSparseAMD(GL_TEXTURE_2D, GL_RGBA, 1024, 1024, 1,
1, GL_TEXTURE_STORAGE_SPARSE_BIT_AMD);
glTexSubImage2D(GL_TEXTURE_2D, 0, 0, 0, 1024, 1024,
GL_RGBA, GL_UNSIGNED_BYTE, data);

## Slide 31: Sparse Textures in OpenGL
Previous example uses glTexSubImage2D
  Driver allocates storage on demand
  Manages physical tile pools for application
  Pass NULL to glTexSubImage*D to de-allocate
  Advantages and disadvantages:
    Pros: simple, easy to integrate, backwards compatible
    Cons: not much control, driver overhead, etc.
glTexSubImage2D(GL_TEXTURE_2D, 0, 0, 0, 256, 256,
GL_RGBA, GL_UNSIGNED_BYTE, NULL);

## Slide 32: OpenGL Texture Tile Pools
Application control of tile pools
  Created new texture targets:
    GL_TEXTURE_1D_TILE_POOL
    GL_TEXTURE_2D_TILE_POOL
    GL_TEXTURE_3D_TILE_POOL
  These resemble array textures
    Fixed element size, unlimited elements
    Cannot directly texture from or render to them
    3D = 3D ‘array’, which otherwise isn’t supported

## Slide 33: OpenGL Texture Tile Pools
Steps to using tile pools:
  Create texture using pool target
  Allocate storage as if it were an array texture
  Associate pool tiles with virtual textures

## Slide 34: OpenGL Texture Tile Pools
Create a tile pool
  Set properties of pool
    Select the type of pool (1D, 2D, 3D)
    Select internal format and tile size
    Set the number of tiles
GLuint tex;
glGenTextures(1, &tex);
glBindTexture(GL_TEXTURE_2D_TILE_POOL, tex);
glTexStoragePoolAMD(GL_TEXTURE_2D_TILE_POOL, // Type of pool
GL_RGBA8, // Internal format
0, // Tile size index
10000); // Number of tiles

## Slide 35: OpenGL Texture Tile Pools
Put data in pools
  2D tile pool looks like 2D array texture
Manipulate pools directly using views
glTexSubImage3D(GL_TEXTURE_2D_TILE_POOL,
0, 0, 0, tile,
256, 256, 1,
GL_RGBA, GL_UNSIGNED_BYTE,
data);
glTextureView(tex, GL_TEXTURE_2D_ARRAY, // Create 2D array texture view
pool, // from this pool
GL_RGBA8, // in this format
0, 1, // with no mipmaps
9000, 1000); // from tile 9000 for 1000 tiles

## Slide 36: OpenGL Texture Tile Pools
Map pool tiles into textures
  Specify an array of tiles to map
  Each has an x, y, z offset and an index
glTexTilePlacementAMD(GL_TEXTURE_2D, // Target
0, // Level
100, // Tile count
xoffsets, yoffsets, zoffsets, // Arrays of offsets
pool, // Pool object
tileindices); // Indices of tiles

## Slide 37: Sparse Textures in Shaders
First and foremost
IT IS NOT NECESSARY TO MAKE SHADER CHANGES TO USE SPARSE TEXTURES

## Slide 38: Extending GLSL – Samplers
Texture type in GLSL is the ‘sampler’
Several types of samplers exist...
  sampler2D, sampler3D, samplerCUBE, sampler2DArray, etc.
We didn’t add any new sampler types
  Sparse textures look like regular textures in shaders

## Slide 39: Reading from Textures
Read textures using ‘texture’
  Built-in function with several overloads:
gvec4 texture(gsampler1D sampler, float P [, float bias]);
gvec4 texture(gsampler2D sampler, vec2 P [, float bias]);
gvec4 texture(gsampler2DArray sampler, vec3 P [, float bias]);
gvec4 textureLod(gsampler2D sampler, vec2 P, float lod);
gvec4 textureProj(gsampler2D sampler, vec4 P [, float bias]);
gvec4 textureOffset(gsampler2D sampler, vec2 P, ivec2 offset [, float bias]);
// ... etc.

## Slide 40: Extending GLSL
Added new built-in functions
  Return residency information along with data
  Most texture functions have a sparse version
  Mix-and match is possible:
    Non-sparse (ordinary) textures appear fully resident
    Sparse textures return undefined data in unmapped regions
int sparseTexture(gsampler2D sampler, vec2 P, inout gvec4 texel [, float bias]);
int sparseTextureLod(gsampler2D sampler, vec2 P, float lod, inout gvec4 texel);
// ... etc.

## Slide 41: Extending GLSL | Sparse Texture
sparseTexture returns two pieces of data:
  Residency status code
  Texel data via inout parameter
int sparseTexture(gsampler2D sampler, vec2 P, inout gvec4 texel [, float bias]);

## Slide 42: Extending GLSL | Sparse Texture
Texel data is returned via inout parameter
  If texel fetch fails, original value is retained
  This is like a CMOV operation
Return code is hardware dependent
  Encodes residency information
  New built-in functions to decode it

## Slide 43: Extending GLSL | Sparse Texture
Residency information returned from fetch
New built-in functions decode it
vec4 texel = vec4(1.0, 0.0, 0.7, 1.0); // Default value
int code;
code = sparseTexture(s, texCoord, texel);
bool sparseTexelResident(int code);
bool sparseTexelMinLodWarning(int code);
int sparseTexelLodWarningFetch(int code);

## Slide 44: Extending GLSL | Sparse Texture
Was texel resident?
  Texel miss is generated if any required sample is not resident, including:
    Texels required for bilinear or trilinear sampling
    Missing mip maps, anisotropic filter taps, etc.
bool sparseTexelResident(int code);

## Slide 45: Sparse Textures – Use Cases
Drop-in replacement for traditional SVT
  Almost... maximum texture size hasn’t grown
Extremely large texture arrays
  Only populate a sub-set of the slices
  Can eliminate texture binds in some applications

## Slide 46: Sparse Textures – Use Cases
Large volume textures
  Voxels, medical applications
  Distance fields + raymarching
    Use maximum step size as ‘default’ value
Variable size texture arrays
  Create a large array texture
  Populate different mip levels in each slice

## Slide 47: Sparse Textures – ARB Extension
The OpenGL ARB adopted sparse textures
  Recent development – released this week
  Slightly different semantics
  Smaller feature set

## Slide 48: Sparse Textures – ARB Extension
ARB version of sparse texture
  Uses texture params + glTexStorage
    No new API
  No shader support
  No tile pool support
  Page sizes queryable
    Uses glGetInternalformativ
    Able to expose more than one selectable page size

## Slide 49: Sparse Textures – Future Work
Increase maximum texture size
Finer control over edge effects
Better residency feedback
Standardize tile shapes

## Slide 50
Thanks!